## Slide 1: CoAP Protocol Negotiation draft-silverajan-core-coap-protocol-negotiation Bill Silverajan TUT Mert Ocak Ericsson

## Slide 2: Summary of changes from -03
Previous drafts used .well-known/core to expose CoAP origin server’s available alternative transports
Discussions in Berlin led towards dropping .well-known/core and using CoRE Resource Directory and CoRE Link Format

## Slide 3: Current changes from -03: Remove link attribute & relation type
”tt” link attribute and ”altloc” links removal (shown in red):
  REQ: GET /.well-known/core
  RES: 2.05 Content
  </sensors>;ct=40;title="Sensor Index", tt="tcp ws sms",
  </sensors/temp>;rt="temperature-c";if="sensor",
  </sensors/light>;rt="light-lux";if="sensor",
  <coap+tcp://server.example.com/>;rel="altloc",
  <coaps+tcp://server.example.net/>;rel="altloc",
  <coap+ws://server.example.com/ws-endpoint>; rel="altloc",
  <coap+sms://001234567>;rel="altloc”

## Slide 4: Proposal in -04: New optional ‘at’ RD parameter
Extend the Resource Directory’s Registration and Update Interfaces
Req: POST coap:/rd.example.com/rd?ep=node1&
at=coap+tcp://server.example.com
Content-Format: 40
Payload:
</sensors/temp>;ct=41;rt="temperature-f"; if="sensor",
</sensors/door>;ct=41;rt="door";if="sensor"
Res: 2.01 Created
Location: /rd/4521

## Slide 5: Proposal in -04: New optional ‘tt’ RD parameter
Extend the Resource Directory’s Lookup Interface
Req: GET /rd-lookup/ep?ep=node5&tt=*
Res: 2.05 Content
<coap+tcp://[FDFD::123]:61616>;ep="node5",
<coap+ws://[FDFD::123]:61616>;ep="node5"

## Slide 6: Advantages
RD provides well-defined interfaces with easy way to extend functionality
Consistent API: Registrations and Updates managed by origin servers based on lifetime values
Group function set provides new possibilities
Support for commissioning tools (via ‘con’)
RD also supports HTTP
DNS SD and DNS-based Service Discvoery may be possible

## Slide 7: Drawbacks
Alternative transport lifetime currently bound to registration lifetime (unless we introduce a new RD parameter)
A simple means for clients to signal a server to temporarily enable an alternative transport (for energy-constrained origin servers) is missing